## Slide 1: CSC201 – Computer Architecture and Microprocessor 8-Bit Fixed-Length Instruction Set for Limited Functionality Machine
Dhruv Agrawal 22114030 Mudit Mangal 22114057

## Slide 2: System Description
Goal
8-bit fixed-length instructions.
Simplified control unit design suitable for embedded or low-power devices.
Registers
Four general-purpose registers (8-bit each).
Program Counter (PC) to track the next instruction.
Zero Flag (ZF) for conditional branching.
Memory
Fixed memory space for program and data storage.
Simulates constrained environments typical of embedded systems
Instruction Format
Create a functional 8-bit fixed-length ISA for a virtual machine.

## Slide 3: Tools Developed
Assembly Parser
Converts human-readable assembly code into machine code.
Instruction Decoder
Decodes and executes machine instructions.
Integration
Ensures correct load, decode, and execute operations.

## Slide 4: Instruction Set Architecture (ISA) Design
Instruction Format:
Fixed-Length Instructions : Uniform 8-bit structure simplifies decoding. Reduces complexity in fetching and interpreting instructions.
Fields : Opcode (4 bits): Specifies the operation (e.g., ADD, SUB, MOV).
Destination (2 bits): Identifies the destination register.
Source (2 bits): Specifies the source register or immediate value
Addressing Modes:
Register Addressing: Operands specified directly by registers.
Immediate Addressing: Operands include a constant value.
Memory Addressing: Data accessed from memory for LOAD/STORE operations.

## Slide 5: Instruction Categories
1. Data Transfer Instructions:
MOV: Move data between registers or from immediate value to register.
LOAD: Load data from memory into a register.
STORE: Store data from a register into memory.
2. Arithmetic and Logical Instructions:
ADD: Add values of two registers.
SUB: Subtract source register value from destination register.
AND: Perform a bitwise AND operation.
OR: Perform a bitwise OR operation.
3. Control Flow Instructions:
JMP: Unconditional jump to a specific memory address.
JZ: Conditional jump if Zero Flag is set.
NOP: No operation, used for delays or alignment.

## Slide 6: Opcode Table
Instruction | Opcode | Description
ADD | 0x0 | Addition of two registers
SUB | 0x1 | Subtraction of one register
MOV | 0x2 | Move data between registers
LOAD | 0x3 | Load data from memory
STORE | 0x4 | Store data to memory
LOADI | 0x5 | Load immediate value to register
JMP | 0x6 | Unconditional jump
JZ | 0x7 | Jump if Zero Flag is set
INC | 0x8 | Increment value in a register
DEC | 0x9 | Decrement value in a register
AND | 0xA | Logical AND operation
OR | 0xB | Logical OR operation
NOP | 0xC | No operation

## Slide 7: Design and Implementation of Components
Assembly Parser:
Converts assembly instructions to binary using predefined opcodes.
Uses an opcodeMap to associate mnemonics with 4-bit binary opcodes.
AssemblyParser::parse reads the assembly file, processes instructions, and outputs machine code for execution.
Instruction Decoder:
Decodes 8-bit machine instructions
Extracts opcode, destination, and source using bitwise operations.
Implements decodeAndExecute to handle arithmetic, data movement, and control flow instructions.
Machine:
Emulates hardware with registers, a program counter, flags, and memory.
Maintains the state modified by the instruction decoder.
Machine::reset initializes or clears CPU state before execution.

## Slide 8: Phases of Execution
Fetch
Fetch Phase:
The Program Counter (PC) sends the address of the next instruction to memory.
The instruction at this address is fetched and temporarily stored for decoding.
Decode
Decode Phase:
The Instruction Decoder reads the opcode and operands from the fetched instruction.
Activates necessary control signals to: Direct data flow by reading data from registers and sending it to the ALU or loading memory addresses.
Execute
Execute Phase:
Control unit directs data flow to ALU, memory, or registers.
Program Counter (PC):Increments to the next instruction for sequential execution. Updates to a new address for jump operations

## Slide 9: Challenges and Solutions
Challenge 1: Limited Operand Size (0–3 Range)
Issue: Operands restricted to 2-bit values (range 0–3).
Solution:
Designed operations to accommodate this limitation.
Used memory or immediate values for larger numbers when needed.
Challenge 2: Encoding Complexity
Issue: Compact 8-bit encoding within a limited opcode space.
Solution:
Adopted a fixed binary format for each instruction.
Allocated remaining bits for operands while maintaining flexibility for future extensions.
Challenge 3: Limited Resources (Registers and Memory)
Issue: Constrained by small memory space and few registers.
Solution:
Managed memory efficiently with a small array.
Optimized register usage for sequential operations.
Challenge 4: Typecasting for Non-Standard Data Types
Issue: u_int8 registers required typecasting for correct printing in C++.
Solution:
Typecast u_int8 values to standard data types (e.g., int).
Ensured compatibility with C++'s print function